Position(Real)
stepPosition(Integer)
cycleTime
Time

---
Initial condition
”scale” is known = steps/mm
initialPosition
initialStepPosition

---
End condition
commandedPosition - 3 examples here

---
StepPosition for end
commandedPosition - 3 examples here
stepPosition =
       floor(commandedPosition*scale)

---
Check for no step
if initialStepPosition == stepPosition
take no step
goto update and return success
commandedPosition
stepPosition

---
Check for too many steps
too high frequency
commandedPosition
stepPosition
commandedPosition
stepPosition
approximateFrequency = abs(initialStepPosition - stepPosition)/cycleTime
if approximateFrequency > maxAllowedFrequency
take no step
goto update and return error

---
Line equations
intitialStepPosition != stepPosition
frequency slow enough
commandedPosition
stepPosition
stepPos = k Time + m
k = (commandedPosition - initialPosition)/cycleTime
m = initialPosition
Time = 0 at initial Time (nominal lcnc time)

---
Check too flat slope
intitialStepPosition != stepPosition, must take step
frequency slow enough
commandedPosition
stepPosition
Avoid problems with numerical precision at flat slope.
k * cycleTime * scale = amount of a step to take
if that amount < 0.01 (for example), just take a step in the
right direction half-way into cycleTime.
We know we must take a step due to previous checks.

---
intitialStepPosition != stepPosition, must take step
frequency range ok
Tstart
Tstart
For positive k:
Tstart = (ceil(initialPosition*scale)-m)/k
For negative k:
Tstart = -(floor(initialPosition*scale)-m)/k
Tstart

---
intitialStepPosition != stepPosition, must take step
frequency range ok
Tstart is known
Frequency
Tstart
Frequency = slope of curve, k * scale
Frequency = k * scale
Tstart

---
intitialStepPosition != stepPosition, must take step
Frequency range ok
Tstart is known
Frequency is known
Number of steps
and direction
commandedPosition
stepPosition
Tstart
nSteps = stepPosition - initialStepPosition
sign(nSteps) = direction
sign(k) = direction
Tstart
commandedPosition
stepPosition

---
Prepare for next cycle
initialPosition <= commandedPosition
initialStepPosition <= stepPosition